## Slide 1: Industrial Communication µ-Projects
Amitojsingh Arora (3238617)
Shunnoy Sarkar (3660409)

## Slide 2: To be noted
We have made the changes in the ISO OSI models.
The Link to our GitHub repo is:
https://github.com/AmitojsinghArora/IndCom

## Slide 3: Contents µ Projects
Modbus RTU, TCP, HTTP
CAN Bus
IO-Link with ESP32 IO-Link Shield

## Slide 4: Modbus Scope
RS485-based communication with Modbus temp/humidity sensor using ESP32.
ESP32 operating as:
    HTTP Webserver (port 80)
    Modbus TCP slave (port 502)
    Wi-Fi Access Point
Sensor data displayed by:
    REST API HTTP Endpoints (/temperature, /humidity)
    Modbus TCP Registers (FC04)
Data visualisation in Node Red.

## Slide 5: Modbus Code Insight
setup() : WiFi initialisation, Modbus RTU and Modbus TCP configuration & HTTP server startup. (node –obj of ModbusMaster; MBserver –obj of ModbusServerTCPasync)
Polling the RS485 sensor:
Sends a Modbus RTU request to the sensor for input registers starting at 0x0000
If true, stores data in global vars.
If false, prints error message.

## Slide 6: Modbus Setup
RS485 to TTL
ESP 32
Modbus Temp/ Hum sensor

## Slide 7: Modbus Communication Interface
PC
RS485
Modbus Temp/ Hum sensor
ESP32
Node Red
Modbus RTU client
App visualization
Modbus TCP Client
80
502
Modbus TCP Server
Modbus RTU Server
Modbus RTU Client & HTTP+Modbus TCP Server
HTTP Server
HTTP Client

## Slide 8: Modbus ISO OSI
Modbus RTU + TCP and HTTP
TCP (port 80 for HTTP and 502 for Modbus TCP)
IP v4 (Wifi AP)
802.11 (Wi-Fi)
RS 485

## Slide 9: Modbus Results

## Slide 10: Outcomes
Mini-tasks done:
    Published time stamp on NodeRed (Intro to NodeRed)
    Controlled an RGB LED over an HTTP server through a Wi-Fi Access Point created by ESP32-s.
Familiarised with Modbus RTU and TCP communication protocols and displaying obtained data over a Webserver via NodeRed.
Used QModMaster for verification of Modbus TCP communication.
Used Wireshark to identify recipient and sender of HTTP requests.

## Slide 11: CAN Bus Scope
Practical introduction to CAN Bus Protocol
    Sending and receiving CAN frames between ESP32 and USB CAN analyzer (connected to PC).
    Adding the application layer (NodeRed) in which CAN data sent by ESP32 is visualised on the dashboard and data sent by serial port by NodeRed would be received by the MCU.
CAN J1939 Protocol Project:
    Recognition of button trigger and rotation of a rotary knob via received CAN frames.
    Controlling of LEDs on keys and segments with transmission of apt CAN frame data.

## Slide 12: CAN Bus Simplified Hardware connections representation

## Slide 13: CAN Bus ISO OSI
SAE J1939
CAN Protocol

## Slide 14: CAN Bus Alternate method: py-can

## Slide 15: CAN Bus Send using py-can
can_serial_write.py:

## Slide 16: CAN Bus Send example

## Slide 17: CAN Bus Receive using py-can

## Slide 18: CAN Bus Receive example

## Slide 19: CAN Bus CR1301 Joystick control approach
Identifying and assigning the PGN, priority, src & dest addresses.
Identifying the keys to their respective labels.

## Slide 20: CAN Bus CR1301 Joystick control approach
3. Assigned two states for the entire system:
i) DEFAULT_POSITION_TRACKING : Segment lights up when rotated clockwise to yellow and changes colour ( as per the colour wheel given in lab manual) after every two shifts in encoder position, thus indicating the position of knob by 12 different colours for 24 identifiable stops.

## Slide 21: CAN Bus CR1301 Joystick control approach
ii) DETECT_DIRECTION: When the knob is rotated clockwise, the change of byte 3 is (bit 5 remains 0, as mentioned in manual, however bit 0 flips):
However when rotated anticlockwise, we observe:
Bits 0 and 5 are 1.
Thus for these triggers, the segment LEDs blink in the corresponding direction.

## Slide 22: CAN Bus Result

## Slide 23: ESP32 and IO-Link device Scope
Transmit sensor data over MQTT via IO Link Master
    Setup MQTT via Mosquitto
    Read data over MQTT Explorer
  eff
  d
Transmit Joystick data from ESP 32 over IO Link shield
    Read joystick data via ESP 32
    Transmit over IO link shield
    Visualize on Node-Red

## Slide 24: ESP32 and IO-Link device Hardware connection and Node-Red
Arduino joystick
Esp 32
Io link shield
Io link master

## Slide 25: ESP32 and IO-Link device ISO OSI model
MQTT + IODD | 
JSON | 
MQTT protocol (Session maintenance) | 
TCP (MQTT on port 1883) | 
IPv4 | 
IO-Link master | MAC on LAN
 | Ethernet IEEE 802.3
ESP32 with joystick
Node Red dashboard

## Slide 26: ESP32 and IO-Link device IO-link master and Node-Red
IO-Link topic generated on IFM Moneo
IO-Link topic
Generation of node red topics

## Slide 27: ESP32 and IO-Link device Node-Red Output

## Slide 28: ESP32 and IO-Link device Node-Red Output

## Slide 29: ESP32 and IO-Link device Challenges and Learning outcomes
Setting up the MQTT Broker over Mosquitto:
    Config file had to be edited
    Mosquitto had to be properly started over CLI
    “C:\Program Files\mosquitto>mosquitto -c mosquitto.conf -v”
Setting up correct IP:
    IO link master needed to have a specific IP (Moneo)
    Laptop needed a static IP on the same subnet mask

## Slide 30: Thank you and best wishes for the exams!