## Slide 1: Industrial Communication µ-Projects
Amitojsingh Arora
Shunnoy Sarkar

## Slide 2: Contents
Modbus RTU
HTTP Requests
Modbus TCP
CAN bus
CAN Joystick
IO link MQTT
ESP32 IO link device

## Slide 3: Modbus RTU, TCP, HTTP Server
Scope:
RS485-based communication with Modbus temp/humidity sensor using ESP32.
ESP32 operating as:
    HTTP Webserver (port 80)
    Modbus TCP slave (port 502)
    Wi-Fi Access Point
Sensor data displayed by:
    REST API HTTP Endpoints (/temperature, /humidity)
    Modbus TCP Registers (FC03)
Data visualisation in Node Red.

## Slide 4: Modbus RTU with HTTP requests
Modbus Temp/Humidity Sensor
RS485-TTL converter
RS-485
Modbus RTU Server
ESP 32
(Wifi Access point &Web server)
HTTP over Wifi
(data in JSON)
Node Red
(Uses HTTP request nodes to acquire sensor values)
Modbus RTU Client & HTTP Server
HTTP Client
PC/Smartphone

## Slide 5: Modbus RTU
Node Red
Modbus RTU(to ESP32)
RS 485 and Temp/Humidity Sensor + ESP32

## Slide 6: Modbus RTU
USB RS 485
Modbus Temp/ Hum sensor

## Slide 7: Modbus RTU, TCP with HTTP requests
Modbus Temp/Humidity Sensor
RS485-TTL converter
RS-485
Modbus RTU Server
ESP 32
(Wi-Fi Access point &Web server)
HTTP
Node Red
(Acquires data through both HTTP and Modbus TCP)
Modbus RTU Client & HTTP+Modbus TCP Server
HTTP+ Modbus TCP Client
Modbus TCP

## Slide 8: Modbus TCP
Node Red
TCP (for Modbus TCP and HTTP)
IP header is added
802.11 (Wi-Fi)+ UART (for Modbus RTU)
RS 485

## Slide 9: Modbus Communication
PC
RS485
RS485
Modbus Temp/ Hum sensor
ESP32
Node Red
Modbus RTU client
App visualisation
Modbus TCP Client
80
502
Modbus TCP Server
Modbus RTU Server
Modbus RTU Client & HTTP+Modbus TCP Server

## Slide 10: Modbus TCP
RS485 to TTL
ESP 32
Modbus Temp/ Hum sensor

## Slide 11: Outcomes
Mini-tasks done:
    Published time stamp on NodeRed (Intro to NodeRed)
    Controlled an RGB LED over an HTTP server through a Wi-Fi Access Point created by ESP32-s.
Familiarised with Modbus RTU and TCP communication protocols and displaying obtained data over a Webserver via NodeRed.
Used QModMaster for verification of Modbus TCP communication.
Used Wireshark to identify recipient and sender of HTTP requests.

## Slide 12: CAN Bus Communication
Scope:
Practical introduction to Controller Area Network (CAN) protocol
Something

## Slide 13: CAN Bus Communication
Scope:
Practical introduction to CAN Bus Protocol
    Sending and receiving CAN frames between ESP32 and USB CAN analyser (connected to PC).
    Adding the application layer (NodeRed) in which CAN data sent by ESP32 is visualised on the dashboard and data sent by serial port by NodeRed would be received by the MCU.
CAN J1939 Protocol Project:
    Recognition of button trigger and rotation of a rotary knob via received CAN frames.
    Controlling of LEDs on keys and segments with transmission of apt CAN frame data.

## Slide 14: CAN Bus
Firmware logic on the ESP32
CAN transport services
CAN protocol: message framing , arbitration, bit stuffing in ESP32 and MCP2515
ESP32 Interface with MCP2515 via SPI

## Slide 15: CAN Bus – Send example

## Slide 16: CAN Bus – Receive example

## Slide 17: Simplified CAN Bus representation

## Slide 18: CR1301 Joystick control approach
Identifying and assigning the PGN, priority, src & dest addresses.
Ientifying the keys to their respective labels.

## Slide 19: CR1301 Joystick control approach
3. Assigned two states for the entire system:
i) DEFAULT_POSITION_TRACKING : Segment lights up when rotated clockwise to yellow and changes colour ( as per the colour wheel given in lab manual) after every two shifts in encoder position, thus indicating the position of knob by 12 different colours for 24 identifiable stops.

## Slide 20: CR1301 Joystick control approach
ii) DETECT_DIRECTION: When the knob is rotated clockwise, the change of byte 3 is (bit 5 remains 0, as mentioned in manual, however bit 0 flips):
However when rotated anticlockwise, we observe:
Bits 0 and 5 are 1.
Thus for these triggers, the segment LEDs blink in the corresponding direction.

## Slide 21: Result

## Slide 22: ESP32 and IO-Link device

## Slide 23: ESP 32 IO link device
Node Red
Modbus RTU
RS 485

## Slide 24: ESP 32 IO link device

## Slide 25: FH Aachen Fachbereich xxx Name Studierende(r) o. Seminar xxx Straße Nr. PLZ Ort